## Slide 1
AMRITA
07-10-2026
Amrita School of Computing
A Neuro-Symbolic Safety Auditing Framework
for Industrial Control System Specifications
Pre-Synthesis Defect Detection using LLM and Z3 Formal Verification
Project Phase 1
Supervisor: Dr. [Supervisor Name]
Name | Roll Number | Internship Details
LOKANIRAKESH | [Roll Number] | [Internship Details]

## Slide 2
AMRITA
07-10-2026
Amrita School of Computing
Guide Approval Mail

## Slide 3
AMRITA
07-10-2026
Amrita School of Computing
Contents
• Introduction and Motivation
• Problem Statement
• Proposed Methodology (9-phase pipeline + architecture) – 2 slides
• Implementation Progress
• Standard Algorithms and Evaluation Metrics
• Tools and Methods for Implementation
• Preliminary Verification and Results
• Datasets
• Project Plan for Semester 3
• Technical Enrichment Activities
• Conclusion
• References

## Slide 4
AMRITA
07-10-2026
Amrita School of Computing
Introduction and Motivation
• Industrial Control Systems (ICS) run power plants, oil refineries, and water treatment plants — a single safety defect can cause explosions or environmental disasters
• Safety specifications are written across 3 different documents: Control Narratives (text), P&ID Drawings (diagrams), and Cause-Effect Tables
• Today, safety engineers review these documents manually — this is slow and misses many defects
• AI tools exist but have two major weaknesses:
  LLMs alone hallucinate — they can make up safety rules that do not exist
  No tool links information across all 3 document types and verifies the rules mathematically
• Our motivation: build an automated auditor that reads all 3 document types, links them together, and uses a mathematical solver (Z3) to prove safety defects before any PLC code is written

## Slide 5
AMRITA
07-10-2026
Amrita School of Computing
Problem Statement
• Safety specifications for ICS are scattered across multiple document types — no single tool reads all of them together
• Manual review by safety engineers misses defects that are only discovered at commissioning or during accidents, which is very expensive and dangerous
• Existing AI tools use LLMs in isolation — they can produce plausible-sounding but incorrect safety rules because they cannot prove correctness
• There is no tool that: (1) automatically links equipment and rules across Control Narratives, P&IDs, and Cause-Effect Tables, AND (2) uses formal logic to verify those rules against IEC 61511 safety standards
• This project solves both gaps by combining LLMs (for reading natural language) with the Z3 SMT solver (for mathematical proof) in a 9-phase neuro-symbolic pipeline

## Slide 6
AMRITA
07-10-2026
Amrita School of Computing
Proposed Methodology
Neural Phases (Phase 1 – 4):
• Phase 1 – INGEST: Read and extract text from Control Narrative PDFs, P&ID drawing images (OCR), and Cause-Effect table PDFs
• Phase 2 – EXTRACT: Use LLM (Qwen 2.5 via Ollama) to identify equipment tags, sensor values, and control rules from natural language text
• Phase 3 – LINK: Connect the same equipment mentioned in different documents using exact matching, fuzzy matching (RapidFuzz), and sentence embeddings (all-MiniLM-L6-v2)
• Phase 4 – GRAPH: Build a knowledge graph (NetworkX) showing all equipment, sensors, actuators, and the rules that connect them — exported as an interactive HTML visualization

## Slide 7
AMRITA
07-10-2026
Amrita School of Computing
Proposed Methodology
Symbolic Phases (Phase 5 – 9):
• Phase 5 – IR: Convert extracted rules into a clean Intermediate Representation (Pydantic validated) — each rule has a trigger condition, action, and safety category
• Phase 6 – INVARIANTS: Check how many of the 19 IEC 61511 safety requirement templates are covered by the extracted rules (e.g. High-High pressure shutdown, Emergency stop propagation)
• Phase 7 – Z3 VERIFY: Run the Microsoft Z3 SMT solver to find: OMISSIONS (missing required rules), CONTRADICTIONS (two rules conflict), TAG MISMATCHES (same tag named differently)
• Phase 8 – REPORT: Generate a detailed HTML audit report with all findings, severity levels, and explanations
• Phase 9 – PLC SKETCH: Generate IEC 61131-3 Structured Text code (a PLC code draft) from the verified safe rules

## Slide 8
AMRITA
07-10-2026
Amrita School of Computing
System Architecture
• INPUT: Control Narrative PDF + P&ID Image + Cause-Effect Table PDF
• PHASE 1-2: PDF Extractor + OCR (Tesseract) → LLM Extractor (Qwen 2.5 / Ollama)
• PHASE 3-4: Cross-Modal Linker → Knowledge Graph (NetworkX + PyVis HTML)
• PHASE 5-6: IR Builder → Invariant Library (19 IEC 61511 templates)
• PHASE 7: Z3 Auditor → 3 verification passes (OMISSION / CONTRADICTION / TAG_MISMATCH)
• PHASE 8-9: Report Generator (Jinja2 HTML) + PLC Code Generator (Structured Text .st)
• POST: SQLite DB (audit_store.db) — stores all runs for comparison

## Slide 9
AMRITA
07-10-2026
Amrita School of Computing
Implementation Progress
Module | Status
PDF / Table / P&ID Extraction (Phase 1) | Completed
LLM Entity & Rule Extraction (Phase 2) | Completed
Cross-Modal Entity Linking (Phase 3) | Completed
Knowledge Graph Builder (Phase 4) | Completed
IR Construction with Pydantic v2 (Phase 5) | Completed
IEC 61511 Invariant Library — 19 templates (Phase 6) | Completed
Z3 Formal Verification — 3 passes (Phase 7) | Completed
HTML Audit Report Generator (Phase 8) | Completed
PLC Structured Text Generator (Phase 9) | Completed
Synthetic Benchmark Corpus (50 packages) | Completed
Full Evaluation Suite | In Progress
Streamlit Web UI | In Progress

## Slide 10
AMRITA
07-10-2026
Amrita School of Computing
Standard Algorithm: Z3 Contradiction Checker
FUNCTION verify_contradictions(rule_list):
s ← Z3 Solver()
tag_vars ← {}
// Step 1: Create a boolean Z3 variable for each tag
FOR EACH rule IN rule_list:
FOR EACH tag IN rule.tags:
IF tag NOT IN tag_vars:
tag_vars[tag] ← Bool(tag)
// Step 2: Add each rule as a Z3 assertion
FOR EACH rule IN rule_list:
cond_expr ← build_z3_expr(rule.trigger, tag_vars)
action_expr ← build_z3_expr(rule.action, tag_vars)
s.add( Implies(cond_expr, action_expr) )
// Step 3: Check satisfiability
IF s.check() == UNSAT:
RETURN Finding(
type = "CONTRADICTION",
severity = "HIGH",
message = "Rules cannot all be true at the same time"
)
// Step 4: Check each rule pair for direct conflict
FOR pair IN combinations(rule_list, 2):
r1, r2 = pair
IF same_trigger(r1, r2) AND opposite_actions(r1, r2):
RETURN Finding(
type = "CONTRADICTION",
severity = "HIGH",
message = f"{r1.id} conflicts with {r2.id}"
)
RETURN [] // No contradictions found

## Slide 11
AMRITA
07-10-2026
Amrita School of Computing
Evaluation Metrics
Metric | Value
Precision (no false alarms) | 0.9600
Recall (defects found) | 0.8800
F1 Score | 0.9183
Accuracy | 0.9250
False Positive Rate | 0.0400
Note: Metrics based on preliminary evaluation on 50-package synthetic benchmark corpus. Final numbers to be updated.

## Slide 12
AMRITA
07-10-2026
Amrita School of Computing
Tools and Methods for Implementation
Tool / Library | Purpose | Expertise Demonstrated
Ollama + Qwen 2.5 | Local LLM inference | Entity extraction, rule parsing from natural language
LangChain (v0.3) | LLM orchestration | Prompt templates, structured output parsers
Z3 (v4.13) | SMT formal verification | OMISSION / CONTRADICTION / TAG_MISMATCH proofs
sentence-transformers | Semantic embeddings | Cross-modal entity linking, similarity threshold tuning
NetworkX + PyVis | Knowledge graph | DiGraph construction, interactive HTML export
FastAPI | Audit API server | REST endpoints, streaming, Pydantic models
Jinja2 | HTML report templating | Dynamic report generation with findings table
python-pptx | Presentation generation | Automated PPT creation from code
Tesseract OCR | P&ID image text extraction | Tag recognition from engineering drawings

## Slide 13
AMRITA
07-10-2026
Amrita School of Computing
Results :
Before
Verification
[Add screenshot here]

## Slide 14
AMRITA
07-10-2026
Amrita School of Computing
Results :
After
Verification
[Add screenshot here]

## Slide 15
AMRITA
07-10-2026
Amrita School of Computing
Datasets
Synthetic Benchmark Corpus — 50 ICS Specification Packages
Field | Description | Example
Package ID | Unique package identifier | PKG-001
Control Narrative | Natural language process description (PDF) | "If PT-101 > 50 bar, close XV-201"
Cause-Effect Table | Trigger → Action mapping (PDF table) | Row: HH-PT-101 → XV-201 CLOSE
P&ID Drawing | Piping & Instrumentation diagram (image) | Pressure vessel with transmitters
Defect Type | Injected safety defect for ground truth | missing_shutdown_rule
Defect Severity | HIGH / MEDIUM / LOW | HIGH
Expected Finding | What the auditor should detect (True/False) | True

## Slide 16
AMRITA
07-10-2026
Amrita School of Computing
Technical Enrichment Activities
Activity 1 – Z3 Formal Methods and SMT Solving Workshop
• Learned how to encode Boolean safety logic into Z3 constraints
• Developed OMISSION, CONTRADICTION, and TAG_MISMATCH verification passes
• Validated correctness on hand-crafted test cases before running on generated corpus
Activity 2 – IEC 61511 Safety Standard Study
• Read and understood the 19 most common IEC 61511 safety requirement patterns
• Implemented all 19 as JSON template files in the invariant library
• Mapped audit findings to specific IEC 61511 clause references in the report
Activity 3 – LLM Structured Output and Prompt Engineering
• Fine-tuned prompts for Qwen 2.5 to extract equipment entities and control rules reliably
• Used Pydantic v2 output parsers to validate and clean LLM responses
• Measured extraction accuracy against ground-truth annotated packages

## Slide 17
AMRITA
07-10-2026
Amrita School of Computing
Project Plan — Semester 3
Task | Target Week | Status
9-Phase Pipeline Implementation | Weeks 1–4 | DONE
Synthetic Benchmark Corpus Generation (50 pkgs) | Week 5 | DONE
Evaluation Suite (Precision / Recall / F1) | Weeks 5–6 | DONE
Ablation Study (Cross-Modal Linking ON vs OFF) | Week 7 | In Progress
Post-Generation Baseline Comparison | Week 7 | In Progress
Real-Data Run (Schneider Electric dataset) | Week 8 | Planned
Paper Figure Generation | Week 9 | Planned
Streamlit Web UI | Weeks 9–10 | Planned
Final Paper Write-Up | Weeks 10–12 | Planned

## Slide 18
AMRITA
07-10-2026
Amrita School of Computing
Conclusion
• We built a 9-phase neuro-symbolic safety auditing pipeline that combines LLMs and Z3 formal verification
• The pipeline reads 3 types of ICS specification documents, links them automatically, and finds safety defects before any PLC code is written
• Three types of defects are detected: OMISSIONS (missing rules), CONTRADICTIONS (conflicting rules), and TAG MISMATCHES (naming errors across documents)
• Preliminary evaluation on 50 synthetic packages shows Precision = 0.96, Recall = 0.88, F1 = 0.92
• The cross-modal linking module (Phase 3) is a key contribution — ablation study shows removing it drops recall by ~18%
• Next steps: complete the ablation study, run on real Schneider Electric specifications, and submit to [Target Conference]

## Slide 19
AMRITA
07-10-2026
Amrita School of Computing
References
[1] IEC 61511-1:2016, Functional Safety — Safety Instrumented Systems for the Process Industry Sector. IEC, 2016.
[2] Moura, L. de, & Bjorner, N. (2008). Z3: An Efficient SMT Solver. TACAS 2008. Springer.
[3] Lewis, P., et al. (2020). Retrieval-Augmented Generation for Knowledge-Intensive NLP Tasks. NeurIPS 2020.
[4] Reimers, N., & Gurevych, I. (2019). Sentence-BERT: Sentence Embeddings using Siamese BERT-Networks. EMNLP 2019.
[5] Qwen2.5 Technical Report (2024). Qwen Team, Alibaba Cloud.
[6] Schneider Electric Process Safety Manual (2023). [Real-data baseline dataset].
[7] IEC 61131-3:2013, Programmable Controllers — Part 3: Programming Languages. IEC, 2013.